| Department of Public Works/Utilities Pumping Stations Checklist Minimum Frequency Quarterly |
| --- |
| Municipality: | Inspection Date: / /201___ |
| Name of Inspector: | Well or Wastewater: |
| Location Surveyed: |
| # | Needs Work | OK | N/A | CONDITION: Write line #’s & comments on back for all “Needs Work” listings, and notify management to initiate required corrective action |

Grounds – NOTE: Municipal water supplies are considered “Critical Infrastructure” by Homeland Security

|  |  |  |  | Station enclosed by a minimum 6 ft. fence? No Trespass Signs? |
| --- | --- | --- | --- | --- |
|  |  |  |  | Station secure: Locked gates, doors or control cabinets? |
|  |  |  |  | Exterior lighting sufficient for all ambient conditions? |
|  |  |  |  | Walkways & grounds level & clear? Snow removed? Grass mowed? |
|  |  |  |  | Door thresholds level & floors slip resistant finish? |
|  |  |  |  | Fire extinguisher here? Mounted? Inspected monthly? Serviced yearly? |
|  |  |  |  | Upset alarms functional? Security alarms for water wells? Monitored? |
|  |  |  |  | Warning signs posted for noise? (if emergency generator present) |
|  |  |  |  | All “Permit Entry Required” Confined spaces identified? Locked? |
| Power Sources - Standby generator? Y N Diesel □ or Natural Gas □ |
|  |  |  |  | “Tie-breaker” crossover electrical switches tested annually? |
|  |  |  |  | All electrical circuits properly & completely identified? |
|  |  |  |  | All electrical outlets are 3-wire grounded? GFCI protected? Tested? |
|  |  |  |  | All panel boxes are tight? Doors closed? No open “knock-outs”? |
|  |  |  |  | Disconnects are labeled for what they control? Locked if Outside? |
|  |  |  |  | Auxiliary generator fuel tanks identified with name & CAS#? |
|  |  |  |  | “Automatic start” warning signs by applicable equipment? |
|  |  |  |  | LOTO supplies, devices & tags available at the station? |
|  |  |  |  | Vapor-tite light fixtures provided? Classified enclosures if needed? |
|  |  |  |  | All power transmission apparatus i.e., belts, shafts correctly guarded? |

Cl2 or SO2 injection, separated from pump?   Y   N   If not present check here N/A □ omit questions 20-26

|  |  |  |  | Sign outside warning of chlorine presence? Oxygen or Cl2 monitoring? |
| --- | --- | --- | --- | --- |
|  |  |  |  | Are all process pipelines identified with content name & flow direction? |
|  |  |  |  | Is emergency SCBA respiratory protection provided? Inspected? |
|  |  |  |  | Visible & audible upset alarms provide pre-entry warning? Tested? |
|  |  |  |  | Gas Tank secured on scale? Hydrostatic test is current? |
|  |  |  |  | Room has both high & low exhaust openings & automatic fan? Working? |
|  |  |  |  | Upset condition alarms are monitored? Report to central station? |

QC Lab Stations:  If not present check here N/A □ omit questions 27-33

|  |  |  |  | All chemical storage in cabinets or on sturdy shelves? |
| --- | --- | --- | --- | --- |
|  |  |  |  | All containers properly labeled? MSDS’s available on site? |
|  |  |  |  | Work areas sufficient for tasks? Adequate lighting? Ventilated? |
|  |  |  |  | All required PPE available? Clean? Adequate? |
|  |  |  |  | Hand wash sink/ potable water, soap, towels available? Trash can? |
|  |  |  |  | Spill kit available? Safety Shower installed? Flowed regularly? Clean? |
|  |  |  |  | Duress alarm, telephone or radio available to report emergencies? |